## Slide 1: PRODUCTIVITY
Dr. Ahmed Elyamany

## Slide 2: Expected Learning Outcome
Define productivity
Differentiate between production rate, efficiency, effectiveness, performance or production.
Know the factors affecting productivity.
Understand the general productivity model.

## Slide 3: Productivity definition
Productivity is the proportion obtained by dividing output by one of the factors of production input.

## Slide 4: Definitions
Efficiency (كفاءة) in general describes the extent to which time or effort is well used for the intended task or purpose.
Effectiveness (فاعلية) means the capability of producing an effect.

## Slide 5: Definitions
Production is concerned with the activity of production goods and services.
Production rate is the quantity of total production produced in unit of time.
Productivity is the ratio of total output produced to the input of one element of production.
Total productivity is the ratio of total output produced to the total inputs used.
It is not necessary that the greater the production, the greater the productivity.

## Slide 6: General Productivity Model
INPUT
OUTPUT
SYSTEM
Capital
Labor
Material
Equipment
Energy
Goods
Services
Transformation

## Slide 7: How to Improve the Productivity
Increase output + decrease input
Increase output + same input
Same output + decrease input
High rate of output increase + low rate of input increase
Low rate of output decrease + high rate of input decrease.
+
-
+
=
=
-

## Slide 8: How to Improve the Productivity
Generally……
  Replace labor with equipment
  Replace old equipment with modern equipment
For developing countries…..
  Lack of money  need for management to increase labor productivity.

## Slide 9: Work Time Component
Lost time due to exceptional conditions
Lost time due to labor shortage
Extra work due to inefficient construction methods
Extra work due to design mistakes
Time consumed in construction if design and specification are correct, equipments are efficient.
Total Work Time
Basic Work Time
Unnecessary Work Time
Inefficient Time
(Poor Management)
Actual Work Time

## Slide 10: Construction Productivity Facts
Labor productivity
  Reach max on Sunday
  Decreases after Tuesday and reach min on Thursday
Best time for labor production is 10am – 12am
Labor need 10-15% of work time as rest time
In repetitive jobs…. Labor productivity decrease after 60:70 min
Average lift capacity is 41,36 kg
Labor productivity is min before lunch time and at the end of the day
labor productivity is max when works 5 days a week, 8 hours a day
Productivity of first shift is more than second shift
Labor productivity affected by overtime for long time
Accidents happen during unproductive time, productive time is safe
Most injuries happen on Saturday and Thursday

## Slide 11: Standard of Living and Productivity
Relation between standard of living and productivity:
Efficient use of inputs decrease the cost of production
The production increases
Amount of output increases.
Cost of input decreases .
Productivity increases.

## Slide 12: Total and Partial Productivity
Total productivity is “the ratio of the total output produced to the total inputs used”
Total Productivity =
Total output
Total inputs
Total Productivity =
Total output
(labor+ material+ equipment) inputs

## Slide 13: Total and Partial Productivity
Partial productivity is “the ratio of the total output produced to the input of one element of production”
Partial Productivity =
Total output
Input of one production element
Labor Productivity =
Total output
Labor input
Material Productivity =
Total output
Material input

## Slide 14: Highest construction productivity
Converting all productive elements inputs into output in order to deliver a quality construction product, achieve maximum cost effectiveness, through the maximum efficient use of resource.

## Slide 15: Measures of productivity
Productivity is not simply performance and not the efficient use of resources , but a combination of both.
Its measurement is carried out by means of ratios:
  Output variables: units produced; products sold; tasks completed; or revenue obtained.
  Input variables: the number of people employed; hours worked; capital used; material costs.

## Slide 16: Labor productivity measures
a) Average labor productivity:
Labor Productivity =
Total output
Labor input
Average Labor Productivity =
Total output
Man-hours of Labor input

## Slide 17: Labor productivity measures
b) Marginal labor productivity:
A measure of the impact on production of the addition of one more unit of labor while keeping other factor fixed.
marginal Labor Productivity =
Increase in output
One unit of Man-hour

## Slide 18: Example 1
A construction company produces 1,000 blocks by employing 40 workers at 7 hours/day for one month. Assume this month has a 25 working days.
What are the production rate and productivity of labor?

## Slide 19: Example 1
Production rate = 1,000 Blocks/month
Labor productivity = 1 Block/ 7 man-hours.
Partial Productivity =
Total output
Input of one production element
Labor productivity =
1,000 Blocks
40 workers
x 25 days
x 7 hrs/day

## Slide 20: Example 2
Suppose this company increased its production to 1,500 Blocks by employing 30 additional workers at 7 hours/day for one month, this month has a 25 working days.
What are the production rate and productivity of labor now?

## Slide 21: Example 2
Production rate = 1,500 blocks/month
Labor productivity = 1 block / 8.2 man-hrs
The production of blocks has gone up by 50%
The labor productivity gone down by 17%
Increased production does not mean increased productivity.
Labor productivity =
1,500 Blocks/month
(40+30) workers
x 25 days
x 7 hrs/day

## Slide 22: Questions
Contact:
Dr. Ahmed Elyamany
019-4100-824
a2hyamany@yahoo.com